## Slide 1
LASER CUT 1/8” ACRYLIC
HOLDER FRAME
1/8” POLYCARBONATE SHEET
FORMED WITH HEAT GUN
ELASTIC BAND
ADHESIVE BACKED FOAM CUSHION
LOW COST EMERGENCY FACE SHIELD

## Slide 2
1
2
3
4
5
6
SOLVENT WELD OR GLUE SLITS
ASSEMBLE ELASTIC STRAP
SOLVENT WELD OR GLUE TOP PART
INSTALL PLASTIC SHIELD THROUGH SLIT
(BENT TO SHAPE WITH HEAT GUN OVER TABLE)
APPLY FOAM WITH ADHESIVE BACK
START WITH BOTTOM

## Slide 3: Fixing The Shield
Drill two small holes in the face shield, secure by wrapping
around the slit with a zip tie

## Slide 4
PART | QTY | 
HOLDERFRAME_BOTTOM_REV0.dxf | 1 | LASER CUT 1/8” ACRYLIC
HOLDERFRAME_TOP_REV0.dxf | 1 | LASER CUT 1/8” ACRYLIC
SHIELDPIECE_REV0.dxf | 1 | 1/8” POLYCARBONATE (CAN CUT BY HAND WITH RAZOR) BENT TO SHAPE WITH HEAT GUN OVER EDGE OF A TABLE
SLIT_A_REV0.dxf | 2 | LASER CUT 1/8” ACRYLIC
SLIT_B_REV0.dxf | 2 | LASER CUT 1/8” ACRYLIC
SLIT_C_REV0.dxf | 2 | LASER CUT 1/8” ACRYLIC
Elastic Strap | 1 | Experiment to find a suitable elastic
Adhesive Foam | 1 | ¼ inch Foam with Adhesive Back (e.g Home Depot Draft Seal Foam) https://www.amazon.com/Weather-Stripping-Density-Sliding-Strips/dp/B07H5948V4/ref=sr_1_2?dchild=1&keywords=draft+seal+foam+1%2F4+inch&qid=1584792766&s=industrial&sr=1-2
Solvent Weld or Glue | 1 | Weld On Acrylic Adhesive or Similar https://www.amazon.com/Weld-Acrylic-Adhesive-Applicator-Bottle/dp/B0096TWKCW